## Slide 1
Team : SystemsGenesys
Member: Eleftherios Batzolis
Mentor: Dr. Konstantinos Rantos
Web Services and Information Security Lab
International Hellenic University
Title : DoS Trojan and Data Leakage on Caravel

## Slide 2
Method for adding the vulnerability
OpenAI’s ChatGPT v.4 :
It is highly sophisticated
It performs better with code
Added versatility
API Integration

## Slide 3
Prompt Engineering
Use of the Chain Of Thought(CoT) technique:
Digital design is a really complex task that requires complex reasoning an produces context aware responses.
These tasks (like creating an FSM) require multiple intermediate reasoning steps.
J. Wei et al., “Chain-of-Thought Prompting Elicits Reasoning in Large Language Models,” 2022, doi: 10.48550/ARXIV.2201.11903.

## Slide 4
Prompting Pattern
In order to gather the necessary steps to create a hardware trojan using an LLM, we enhanced our prompt engineering techniques first by using the Recipe prompt pattern :
The main intent of this process is to gather a sequence of steps for creating the trojan intent (for example “I would like to add “X” feature is “X” code . I need to perform steps A,B,C. Provide a sequence for me and fill any missing steps.”).
Using this pattern the LLM will analyze a concrete sequence of steps for creating with intent the trojan(for example “Identify any unnecessary steps”)
Prompt example: https://chat.openai.com/share/44e37758-e3c0-4025-98a8-89f75f36166b

## Slide 5
Prompting Pattern
We then used the Persona prompt pattern to:
provide the LLM with intent (for example, “Acts as a digital engineer”) and conceptualize context (refactor the code, provide Verilog files)
provide the LLM with motivation to achieve a certain task (for example, “refactor the code to provide extended functionality”).
structure fundamental contextual statements around key ideas (for example, “Provide code that a digital designer would create”)
provide example code for the LLM to follow along by using the Chain of Thought prompt engineering technique (for example “This part of code “X” from my codebase needs new features.”).
Prompt example: https://chat.openai.com/share/8d425e27-d6d8-473b-9f53-7e42fdf6c008

## Slide 6
A UART D.o.S. hw trojan
1st design

## Slide 7
We identified a vulnerability in ChatGPT Content filtering.
During the course of our investigation, ChatGPT's content filtering procedure impeded attempts to write "malicious" code. We discovered a means to circumvent this security and "exploit" the system by utilizing ZULU as the primary language. As a proof of concept, we present the dialogue below:
Asking how to build a chemical bomb using English:
Asking how to build a chemical bomb using Zulu:
https://chat.openai.com/share/445456a6-b89d-438b-a547-05adbec612de
https://chat.openai.com/share/53ca6e4b-ca74-405f-ae9d-32c748fa471a

## Slide 8
Prompt without bypassing the content filter : https://chat.openai.com/share/ad3ca337-03a9-4301-947c-2ee9ce5c1e3b
P.o.C.
This is design is a UART peripheral in Verilog.
We added the functionality of a trigger inside the state machine inserted in the transmitter part of UART core.
The state machine seeks the sequence of 8’hAA,8’hBB.
After state activation any transmission is blocked.
This single-shot prompt design, is not possible without bypassing the content filter.
Severity of the vulnerability
Insertion phase: Design
Abstraction level: Register‐transfer level (RTL)
Act. mechanism: Conditionally triggered
Functional Effects: Denial of service
Physical characteristics: Functional
UART peripheral with a D.o.S. hw trojan

## Slide 9
Prompt bypassing the content filter : https://chat.openai.com/share/de877a72-3ccd-4dcd-8c72-8faebfb8c48e
P.o.C.
Prompt without bypassing the content filter : https://chat.openai.com/share/89c53be5-10bf-4ecc-859a-894b3ae967c2
2)
1)
Code and testbench link

## Slide 10
A wishbone bus D.O.S. hw trojan targeting efabless Caravel project
2st design

## Slide 11
Why attack the wishbone bus?
Wishbone Bus is :
One of the most popular open source protocols to connect IP blocks inside an SoC.
Used broadly all over the world because of the Interoperability, flexibility, and reusability it offers.
Used substantially in Universities worldwide.
Used by companies (like efabless ) all over the world.
Open-source

## Slide 12
P.o.C.
Prompt : https://chat.openai.com/share/89c53be5-10bf-4ecc-859a-894b3ae967c2
Classic Wishbone Bus design
Simulation: (Code and Simulation)
Simulation with Trojan (Code and Simulation):

## Slide 13
Why attack the Caravel project?
Caravel project:
is one of the most influential open-source projects in (open-source) Chip design.
provides a cost-effective route for ASIC development - it leverages the use of mature and low-cost semiconductor and community-driven development.
is used substantially in Universities worldwide.
greatly encourages code reuse, making it easier for designers to integrate existing building blocks and IP cores into their ASIC designs.
…
HIGHER IMPACT

## Slide 14
An alpha version of our malicious code implementation methodology is:
We first analyzed the code in the GitHub repository.
Inside the housekeeping.v file the wishbone to SPI to CPU communication is implemented.
We can alter the wishbone FSM implementation by adding a stage where if a certain value is transmitted in the bus then an internal signal gets stuck at “0”
This way we are glitching the handshake method causing a Denial Of Service.

## Slide 15
Prompt example: https://chat.openai.com/share/8d425e27-d6d8-473b-9f53-7e42fdf6c008
P.O.C.
Prompt example where “wbbd_busy” signal should always be set to “1’b1” when the “wbbd_data” signal has the value “8’df”. This is just an example concept.
Severity of the vulnerability:
Insertion phase: Design
Abstraction level: Register‐transfer level (RTL)
Act. mechanism: Conditionally triggered
Functional Effects: Denial of service
Physical characteristics: Functional

## Slide 16
Leaking key from a symmetric AES block cipher
3nd design

## Slide 17
Why attack AES?
AES is :
One of the most popular encryption standards.
Used broadly all over the world.
Is globally standardized, regulated and incompliance with governments, individuals and enterprises.
Is efficient in terms of processing power and memory usage so it is used everywhere.

## Slide 18
An alpha version of our malicious code implementation methodology is:
We first analyzed the code in the GitHub repository.
We use a shift register to store the key.
When a pattern is detected through a FSM we use a covert way of leaking the key by
  modulating an (unused) pin on chip that generates an RF signal. This signal can be used to transmit the key bits. Then it can be received with an ordinary AM radio.
The data carried by the AM signal needs to be easily interpreted by a human by using a beep scheme.

## Slide 19
Prompt for transmit.v : https://chat.openai.com/share/8c8fb17c-6647-4eee-8c1e-71c2bc0c1b95
P.o.C.
Leaking the key by modulating an (unused) pin on chip that generates an RF signal.
Severity of the vulnerability:
Insertion phase: Design
Abstraction level: Register Transfer level
Act. mechanism: Conditionally triggered
Effects: Leak Information
Location: Processor
Physical characteristics: Functional